## Slide 1
Prototyping the Network Model using Packet Tracer

## Slide 2: Introduction
Cisco Packet Tracer is a powerful network simulation program that allows students to experiment with network behavior.
Packet Tracer provides simulation, visualization, authoring, assessment, and collaboration capabilities and facilitates the teaching and learning of complex technology concepts.
Students can build, configure, and troubleshoot networks using virtual equipment and simulated connections.

## Slide 3: Interface overview
Area 1: Menu bar – This is a common menu found in all software applications; it is used to open, save, print, change preferences, and so on.
Area 2: Main toolbar – This bar provides shortcut icons to menu options that are commonly accessed, such as open, save, zoom, undo, and redo, and on the right-hand side is an icon for entering network information for the current network.
Area 3: Logical/Physical workspace tabs – These tabs allow you to toggle between the Logical and Physical work areas.
Area 4: Workspace – This is the area where topologies are created and simulations are displayed.
Area 5: Common tools bar – This toolbar provides controls for manipulating topologies, such as select, move layout, place note, delete, inspect, resize shape, and add simple/complex PDU.

## Slide 4: Contd..
Area 6: Realtime/Simulation tabs – These tabs are used to toggle between the real and simulation modes. Buttons are also provided to control the time, and to capture the packets.
Area 7: Network component box – This component contains all of the network and end devices available with Packet Tracer, and is further divided into two areas:
  Area 7a: Device-type selection box – This area contains device categories
  Area 7b: Device-specific selection box – When a device category is selected, this selection box displays the different device models within that category
Area 8: User-created packet box – Users can create highly-customized packets to test their topology from this area, and the results are displayed as a list.

## Slide 5: Packet Tracer Modes
Cisco Packet Tracer provides two operating modes to visualize the behavior of a network
  Real-time mode
  Simulation mode
The real-time mode gives a viable alternative to real equipment and allows them to gain configuration practice before working with real equipment.
In simulation mode the user can see and control time intervals, the inner workings of data transfer, and the propagation of data across a network.

## Slide 6: Protocols supported:

## Slide 7: Cisco devices and Packet Tracer devices
The following routers are available in Packet Tracer:
Cisco 1841: This is an Integrated Service Router (ISR) having two Fast Ethernet ports, two slots for High Speed WAN Interface Cards (HWICs), and one slot for Advanced Integration Module (AIM)
Cisco 1941: This is similar to the previous model but runs on Cisco IOS Version 15. It has two ports that operate at Gigabit Ethernet speeds.
Cisco 2620XM: This is a multiservice router with one Fast Ethernet port, two slots for WAN Interface cards, and one slot for AIM.
Cisco 2621XM: This is similar to the previous model, except that this router has two Fast Ethernet ports.

## Slide 8: Contd..
Cisco 2811: This ISR comes with two Fast Ethernet ports, four WIC slots, and a dual slot for AIM.
Cisco 2901: This router has two Gigabit Ethernet ports, four WIC slots, and two Digital Signal Processor (DSP) slots. This router uses Cisco IOS Version 15.
Cisco 2911: This router has three Gigabit Ethernet ports and all the other features of the previous router. It runs on IOS Version 15.
Generic Router-PT: This is a custom router running on Cisco IOS. It contains 10 slots and has separate modules with a naming convention beginning with PT.

## Slide 9
The following switches are available in Packet Tracer:
Cisco 2950-24: This managed switch comes with 24 Fast Ethernet ports.
Cisco 2950T-24: This switch is a member of the Catalyst 2590 Intelligent Switch family and has two Gigabit Ethernet ports in addition to the 24 Fast Ethernet ports.
Cisco 2960-24TT: This is another 24 port switch;
Cisco 3560-24PS: This switch is different from the others because it is a layer 3 switch that can be used to perform routing in addition to switching.
Bridge PT: This is a device used to segment a network and it has only two ports (which is why it is a bridge; if it had more, it'd be called a switch).
Generic Switch PT: This is a Packet-Tracer-designed switch running on Cisco IOS. This is the only customizable switch with 10 slots and several modules.

## Slide 10: Connecting devices
Copper straight-through: This is a standard Ethernet cable that is used to connect two devices that operate in different layers of the OSI model (such as hub to router and switch to PC). It can be used with Ethernet, Fast Ethernet and Gigabit Ethernet port types.
Copper cross-over: This Ethernet cable connects devices operating in the same OSI layer (such as hub to hub, PC to PC, PC to router, and PC to printer). This cable can also be used with Ethernet, Fast Ethernet and Gigabit Ethernet port types.
Fiber: This cable connects Fast Ethernet and Gigabit Ethernet ports of a fiber port.
Serial DCE and DTE: Serial cables connect routers together and connect routers to the cloud.
  The DCE (Data Circuit-terminating Equipment) end has a clock symbol on it. Clocking must be enabled on this end using the clock rate <300-4000000> command to bring the line protocol up. If Serial DTE (Data Terminal Equipment) is chosen, the first device connected with this cable will be the DTE end and next device will be the DCE end.